## Slide 1: The endangered Species Act: Navigating the New Pesticide Labels
Purdue University is an Equal Access / Equal Opportunity institution.

## Slide 2: Office of the Indiana State Chemist
Mitch Trimble
jmtrimbl@purdue.edu
Nate Davis Manager of Certification and Licensing davi1280@purdue.edu
765-494-7108
Located at Purdue University
175 S University St.
W. Lafayette, IN 47907
www.oisc.purdue.edu
765-494-1492
Notes: https://myplate-prod.azureedge.us/sites/default/files/2024-04/MyPlatePoster-White20x16.pdf
https://extension.purdue.edu/news/county/elkhart/2023/03/how-to-build-a-balanced-breakfast.html

## Slide 3: Questions? Can also call or text here!

## Slide 4: Labels will be transitioning
Updates will continue as pesticides are added and updated.
Process for pesticide approval has changed so the new labels reflect these changes.
Labels have the new ESA (Endangered Species Act) required elements.
Two specific changes
  Physical changes within the label
  New web-based requirements outside of the physical label that will need to be addressed.
Notes: https://myplate-prod.azureedge.us/sites/default/files/2024-04/MyPlatePoster-White20x16.pdf
https://extension.purdue.edu/news/county/elkhart/2023/03/how-to-build-a-balanced-breakfast.html

## Slide 5: Label Example- Looking into the new changes
All new products will have the new label.
As products are reregistered, the label will be updated.
The products you already have may not have the newest label.

## Slide 6: Label Example- Mandatory Spray Drift Buffers
Mandatory Spray Drift Buffers
Section 9
Not a new section to the label, but it has changed.
Biggest change:
  Downwind buffer will be on every label.
  Have the option to mitigate (reduce) the buffer.

## Slide 7: Label Example- Mandatory Runoff Mitigation
Mandatory Runoff Mitigation
Section 11
Not a new section to the label, but it has changed.

## Slide 8: Label Example- Mandatory Runoff Mitigation Cont.
Biggest change:
  “You must achieve a minimum _____ points for crop listed on this label unless otherwise stipulated below.”
  Each pesticide will have a value of 0-9 points
  Generally easy to achieve
  3 points most common
Must check PULA (Pesticide Use Limitation Area) within 6 months of application
  Check if target field is in a PULA. It could make stricter regulations on your specific pesticide.
  If your target area and application pesticide fall within a PULA, you will need to read the Bulletin in the BLT (Bulletins Live! Two) website. More information on how to do that!
    https://www.epa.gov/pesicides/bulletins
    EPA mitigation Menu Website: https://www.epa.gov/pesticides/mitigation-menu

## Slide 9: Label Example- Mandatory Runoff Mitigation Cont.
This web based content is an extension of the label and YOU MUST FOLLOW THEM. This will be the new format of the label.

## Slide 10: Label Example- Endangered and Threatened Species Protection Requirements
Endangered and Threatened Species Protection Requirements
Section 12
“You must obtain any applicable Endangered Species Protection Bulletins (Bulletins) within 6 months prior to or on the day of application.”
  https://www.epa.gov/pesticides/bulletins
Can call and leave a voicemail. They will call you back.
  1-844-477-3813
  Or Email ESPP@epa.gov

## Slide 11: Summary of New Label Section Requirements to Look For

## Slide 12
PULAs and Bulletins

## Slide 13: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
“You must obtain any applicable Endangered Species Protection Bulletins (Bulletins) within 6 months prior to or on the day of application.”
Let’s check to see if we need to add any point (have stricter requirements) to use this pesticide(s).
  Add your location address
  Add application month
  Add the EPA Registration number of the pesticide from the label.
Website does have tutorial to help!
Map can zoom in and out. And can change to 3D map to see field boundaries.
https://www.epa.gov/pesticides/bulletins

## Slide 14: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
You are searching for the areas in PINK. Those are the PULAs (Pesticide Use Limitation Areas).
  PULAs are areas that have additions restrictions on the pesticide(s) that are being looked up.
  Area will change as different pesticides are searched.
https://www.epa.gov/pesticides/bulletins

## Slide 15: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Add target Field or location
https://www.epa.gov/pesticides/bulletins

## Slide 16: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Change Application Month
  Per the label, you can look up within 6 months of application.
  You will have to do this for every target field.
  Can do this on rainy days or off season.
  Just selects MONTH, not the day.
https://www.epa.gov/pesticides/bulletins

## Slide 17: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Add EPA Registration Number
  MUST search by Reg Number, not name.
  Found on first page of product information.
https://www.epa.gov/pesticides/bulletins

## Slide 18: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Add EPA Registration Number
  MUST search by Reg Number, not name.
  Found on first page of product information.
https://www.epa.gov/pesticides/bulletins

## Slide 19: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Once all information is in. You will see if there is a PULA for your selected pesticide.
For this example, there is NO PINK, so there is no PULA  NO additional restrictions on this product in this target area.
This is web based, as you move the map it will update for additional Bulletins.
  If “Printable Bulletin” is green you have loaded all appropriate bulletins for this target area.
https://www.epa.gov/pesticides/bulletins

## Slide 20: Bulletin Live! Two Website
Endangered and Threatened Species Protection Requirements
Click “Printable Bulletin” to download the Bulletin for this target area and pesticide.
STRONGLY RECOMMENDED TO SAVE THESE OR PRINT THEM FOR YOUR RECORDS AS PROOF THAT THESE WERE CHECKED.
https://www.epa.gov/pesticides/bulletins

## Slide 21: Bulletin Live! Two Website- Bulletins
Endangered and Threatened Species Protection Requirements
Example of a “Bulletin”
  Shows map of target area
  Shows any Limitation Areas
  NO CURRENT REQUIREMENT FOR RECORD KEEPING.
    Not required however, maps can change at any time! Changes are made as products are registered, reregistered, or as endangered species are updated.

## Slide 22: Bulletin Live! Two Website- Tank Mixes
Endangered and Threatened Species Protection Requirements
ALSO can use multiple products under one search.
  Example: a tank mix with multiple products
  Will be in this example
  In tank mix, you will have to follow the MOST STRICT guidelines listed on the labels.
    Highest downwind buffer requirements
    Highest point system
    Most strict BLT
Example of a “Bulletin” WITH PULA using the same product as a tank mix.

## Slide 23: Bulletin Live! Two Website- PULA with a Bulletin as a Tank Mix
Endangered and Threatened Species Protection Requirements
Example of a “Bulletin” with a PULA
  Shows map of target area that has a PULA associated with these pesticides.
  This example has more than one pesticide listed under the search.

## Slide 24: Bulletin Live! Two Website- PULA with a Bulletin as a Tank Mix
Endangered and Threatened Species Protection Requirements
Example of a “Bulletin” with a PULA
  Click on target field.
    Printable Bulletin should be Green.
    Blue and White box on the left should change and show “Limitations for Selected Areas”
  Can select “Full Details” to have a quick look at limitations.
  Download the Bulletin for full details and limitations.

## Slide 25: Bulletin Live! Two Website- PULA with a Bulletin as a Tank Mix

## Slide 26: Bulletin Live! Two Website- PULA with a Bulletin as a Tank Mix
Endangered and Threatened Species Protection Requirements
Example of a “Bulletin” with a PULA
  Will provide additional information for Pesticide Use Limitations.
    Pesticide Use Summary Table
    Codes and Limitations Table
      Will show the actual limitations for using this product(s).
Not required to save this but it is strongly suggested.

## Slide 27: Bulletin Live! Two Website- After checking for PULA
If your search shows no additional PULAs.
  Follow application directions as the label is listed.
  For THIS example (Using Liberty Ultra, in Indiana, with No PULA):
    Must reach the 10ft downwind buffer.
    Must obtain the 3 mitigations points required.
Next Step
  Check Spray Drift Buffer Calculator to see if we can reduce downwind buffer.

## Slide 28
Spray Drift Buffer Tools

## Slide 29: Spray Drift Buffer Calculator Tools
EPA provides THREE ways to do this calculation
  Use Pesticide Ecological Spray Drift Buffer Calculation Worksheet
    Paper worksheet that can be printed
    Calculations are manual. Must be careful not to make any errors.

## Slide 30: Spray Drift Buffer Calculator Tools
EPA provides THREE ways to do this calculation
  Use Pesticide Ecological Spray Drift Buffer and Runoff Calculation Excel Spreadsheet
    Microsoft Excel template
    Calculations are completed within the template.
    Best for those familiar with Excel
    Can be more difficult to use.
    Same spreadsheet to calculate Runoff/Erosion mitigation points (will show that later on).
    Select the Drif Field tab below.

## Slide 31: Spray Drift Buffer Calculator Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    PALM- “Pesticide App for Label Mitigation”
    Web based, not a phone “app” but can be used on your phone using the web browser.
    Easiest to use.
    www.epa.gov/pesticides/pesticide-app-label-mitigations
    Will use this website for Spray Drift Calculator AND Run off Erosion Calculator.
    Select “Spray Drift Calculator” to get started.

## Slide 32
Using EPA PALM Website
Step by Step Guide to calculating, and reducing spray drift buffers

## Slide 33: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Will ask questions.
  Goes step by step as you answer

## Slide 34: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Question 1:
    Did the label or Bulletin you downloaded require you to have a buffer?
      Y? N?

## Slide 35: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Has option fields but this information will be added to the printout at the end.
    Best for record keeping.

## Slide 36: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Application Type
      This example will use Ground boom

## Slide 37: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Conditions Not Requiring Ecological Spray Drift Buffers.
      Several questions:
        If you can answer YES to ANY of these questions, you will no longer require a spray drift buffer AT ALL.
        Look for “Skip to Final Summary” if you have met these requirements.
          No other questions need answered.

## Slide 38: Bulletin Live! Two Website- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Conditions Not Requiring Ecological Spray Drift Buffers.
      Several questions:
        If you can answer YES to ANY of these questions, you will no longer require a spray drift buffer AT ALL.
        Look for “Skip to Final Summary” if you have met these requirements.
          No other questions need answered. You are DONE.

## Slide 39: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Conditions Not Requiring Ecological Spray Drift Buffers.
      Several questions:
        If you can answer YES to ANY of these questions, you will no longer require a spray drift buffer AT ALL.
        Look for “Skip to Final Summary” if you have met these requirements.
          No other questions need answered. You are DONE.

## Slide 40: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Conditions Not Requiring Ecological Spray Drift Buffers.
      Several questions:
        If you can answer NO to all of these questions you will need to continue to the next step.
        This will be the more common situation.

## Slide 41: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Product Specific Application Information
      Several questions:
        Information from the Label and Bulletin for the Product(s) you have.
        Allows for some flexibility of application to mitigate the buffer size.

## Slide 42: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Product Specific Application Information
      Several questions:
        Information from the Label and Bulletin for the Product(s) you have.
        Allows for some flexibility of application to mitigate the buffer size.
        Liberty Ultra Example
          MEDIUM Droplet size = 10 ft Buffer

## Slide 43: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Product Specific Application Information
      Several questions:
        Liberty Ultra Example

## Slide 44: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Ground Application Ecological Drift Buffer Reduction Options
      Several questions:
        Allows for some flexibility of application rate to mitigate the buffer sizer.
        Find information from the product label for Max Labeled Application Rate (what is the max rate)
        Liberty Ultra Example
          What rate we will use for Planned Application Rate.
          Is there a reduction in the buffer from the change of rate?
          Application Rate and Max rate the Same NO Reduction

## Slide 45: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Ground Application Ecological Drift Buffer Reduction Options
      Several questions:
        Allows for some flexibility of application rate to mitigate the buffer sizer.
        Find information from the product label for Max Labeled Application Rate (what is the max rate)
        Liberty Ultra Example
          What rate we will use for Planned Application Rate.
          Is there a reduction in the buffer from the change of rate?
          Application Rate less (CANNOT be less than the label minimum rate) than Max rate

## Slide 46: EPA PALM- Calculating “Ecological Spray Drift Buffer Reduction”
We will use the EPA PALM website to calculate the Spray Drift Buffer Reduction for our example.
  Next Question
    Ground Application Ecological Drift Buffer Reduction Options
      Several questions:
        Liberty Ultra Example
          Always look for the “Skip to Final Summary” button at the bottom. If you have reduced the buffer to ‘0’, you can skip to the end.
          Even if there is other unanswered questions.
          Additional questions help to reduce the buffer, only if needed.
          Suggested to download/print the summary for your records.

## Slide 47
Runoff/ Erosion Mitigation Calculation Tools

## Slide 48: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use Pesticide Runoff/Erosion Mitigation Points Calculation Worksheet
    Paper worksheet that can be printed
    Calculations are manual. Must be careful not to make any errors.

## Slide 49: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use Pesticide Ecological Spray Drift Buffer and Runoff Calculation Excel Spreadsheet
    Microsoft Excel template
    Calculations are completed within the template.
    Best for those familiar with Excel
    Can be more difficult to use.
    SAME spreadsheet as the Spray Drift Buffer.
      Calculations on a separate tab below.
      Select Runoff Field ID below

## Slide 50: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    PALM- “Pesticide App for Label Mitigation”
    Easiest to use.
    www.epa.gov/pesticides/pesticide-app-label-mitigations
    Select “Runoff/Erosion Calculator” to get started.

## Slide 51: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    PALM- “Pesticide App for Label Mitigation”
    Easiest to use.
    www.epa.gov/pesticides/pesticide-app-label-mitigations
    Select “Runoff/Erosion Calculator” to get started.

## Slide 52: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Question 1:
      Enter Field, Product, Crop information

## Slide 53: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Evaluate the farm/field(s) being treated
      Similar to the first page of the Drift Buffer page. If you can select YES by clicking ANY of these options, you will fulfill your required “Points”.
        Look for “Skip to Final Summary” bottom if you have met these requirements.
          No other questions need answered. You are DONE. Download/Print for records as suggested

## Slide 54: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Evaluate the farm/field(s) being treated
      Not common to select any of these options
      If you are unsure on the description or if these apply click the “View the description of this measure” to get more information and the definition on the requirement.
      Click “None of the Above” box at the bottom of the page

## Slide 55: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Pesticide Label Points
        Add the required amount of points for your specific product.
        Use the highest point number if there is a tank blend.
        Found on the label

## Slide 56: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Pesticide Label Points
        Liberty Ultra Example
          Requires 3 points
        The top of the page will continue to update as you go through the questions.

## Slide 57: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Systems that Capture Runoff and Discharge
      If any apply, points will be added.
      If not applicable, points will be 0, cont to next question.
      This example, Not Applicable.

## Slide 58: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Mitigation Relief Based on Pesticide Runoff Vulnerability
        Most important to select State and County of application.
        Each county is awarded Points just by location on how likely runoff will occur in that county and how waterways are in that County.
        There are some counties that have 0 points.

## Slide 59: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Conservation Program, Runoff/Erosion Specialist, and Mitigation Tracking
        Select YES for Mitigation Tracking. That is what we are doing right now.
          Will give points for tracking.
          Would give a total of 3 points for LIBERTY ULTA example and we would be done.

## Slide 60: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Conservation Program, Runoff/Erosion Specialist, and Mitigation Tracking
        Select YES for Mitigation Tracking. That is what we are doing right now by filling out this calculator tool.
          Will give points for tracking.
          Would give a total of 3 points for LIBERTY ULTA example and we would be done.
          (We will select no to continue on this Tutorial)

## Slide 61: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Field Characteristics
        Add specific characteristics per field
        Slope and soil types
          Flatter fields get awarded more points
          More sandy soils get awarded more points
        Good resource for finding soil types by exact locations: Web Soil Survey https://websoilsurvey.nrcs.usda.gov/app/

## Slide 62: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      In Field Mitigation Measures
        Gives MANY more options to get points awarded.

## Slide 63: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Field –Adjacent Mitigation Measures
        Gives MANY more options to get points awarded.

## Slide 64: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Other Mitigation Measures
        Gives MANY more options to get points awarded.

## Slide 65: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Application Parameters (optional)
        If you STILL needed points at the very end.
        Allows you to add the Maximum Labeled Annual Application Rate found on the Label. AND The Planned Annual Application Rate
        Lower rates (not lower than label minimum) will award points.

## Slide 66: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Application Parameters (optional)
        If you STILL needed points at the very end.
        Allows you to add the Maximum Labeled Annual Application Rate found on the Label. AND The Planned Annual Application Rate
        Lower rates (not lower than label minimum) will award points
          Max is 29, actual planned application is 19
          This example, awarded 2 Points

## Slide 67: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Resulting Mitigation Points
      Final Results

## Slide 68: Runoff/Erosion Mitigation “Points” Calculation Tools
EPA provides THREE ways to do this calculation
  Use EPA PALM
    Next Question:
      Resulting Mitigation Points
      Final Results
      Print/download

## Slide 69: Summary of New Label Section Requirements to Look For

## Slide 70
Resources

## Slide 71: Resources
EPA Mitigation Menu- Has definitions and additional Information
  www.epa.gov/pesicides/mitigation-menu
  Also has step by step what you would need to do.
EPA Pesticide and Endangered Species Educational Resources Toolbox
  www.epa.gov/endangered-species/pesticides-and-endangered-species-educational-resources-toolbox
  Guidance documents, handouts, presentations, webinars, and other resources
  Download the Spray Drift and Runoff Mitigation Calculator Spreadsheet here
  Download the Spray Drift and Runoff Mitigation Calculator paper worksheet here
Crop Life America
  www.croplifeamerica.org
  www.croplifeamerica.org/esa
  3rd party organizations with great information
  Has YouTube videos and other helpful resources

## Slide 72: Resources
YouTube Video- That follows this handout
  How to Comply with the Endangered Species Act
  https://www.youtube.com/watch?v=sZex6gYGhT0

## Slide 73: Resources
Crop Life America- Very short YouTube Videos
Adapting to ESA: Mitigating Overview https://youtu.be/BWlgBhgephY?si=NJhyPifvpQrfOSkk
Adapting to ESA: Bulletin Live! Two
https://youtu.be/_ayFOsYQCLs?si=C7lvI59ero-l64JG
Adapting to ESA: Spray Drift
https://youtu.be/V_sM0Q9s2Ho?si=cCjkCdL4lqsA3vmm
Adapting to ESA: Runoff https://youtu.be/2CpXDR23PHw?si=T0WTmW2009BRIEyK
Find all of these on the CropLife America YouTube Channel @croplifeamerica

## Slide 74: Questions? Contact the Officed of the Indiana State Chemist
Mitch Trimble
jmtrimbl@purdue.edu 765-494-1492
Nate Davis Manager of Certification and Licensing davi1280@purdue.edu
765-494-7108
Located at Purdue University
175 S University St.
W. Lafayette, IN 47907
www.oisc.purdue.edu
Notes: https://myplate-prod.azureedge.us/sites/default/files/2024-04/MyPlatePoster-White20x16.pdf
https://extension.purdue.edu/news/county/elkhart/2023/03/how-to-build-a-balanced-breakfast.html